# Introduction
The NV APB Ethernet is a simple Ethernet solution for FPGA. Main motivation was to use Ethernet using VexRiscV and VIHAL

# Main Features
- Simple APB only interface for soft-CPU control
- VIHAL (https://github.com/nvitya/vihal) drivers available for VRV100 (VexRiscV)
- No bus mastering
- VHDL implementation
- Multi packet buffering up to 8 packets
- Selectable TX and RX memory size between 4 kByte - 16 kByte
- Selectable TX and RX maximum packet size (slot size)
- Supported PHY protocols: MII, RMII, GMII (RGMII has tx problems yet)
## How it Works
The NV APB Ethernet contains two relatively large internal buffers for Ethernet packet sending and receiving: TXMEM and RXMEM. Their size can be selected at synthesis time between 4 kByte and 16 kByte. Both RXMEM and TXMEM are divided into fixed-size slots. The slot size can be selected by a register, which determines the maximal length of the transmit and receive packets. The maximal standard ethernet packet length is 1536 Bytes (including CRC). If the slot size is set to 1536 bytes = 384 32-bit words then having 4 kByte RXMEM results in two slots. Setting the slot size to 1364 Bytes gives 3 slots. Maximum 8 slots are supported, also there is no reason to set the slot size smaller than 512 Bytes for 4 kByte RX/TX memory.

At the RX packets the CRC (last four bytes of the Ethernet packet) must fit into the RX slot too, otherwise the packet will be dropped with OVF (overflow) error.

The RX and TX memories are organized into 32-bit words.
The RX memory is read-only from the CPU side (APB bus), write-only from the Ethernet side. The TX memory is write only from the CPU side and it is read only from the Ethernet side. (It is possible to make the TX memory CPU readable too, but then it will use twice as much RAM.)

The slot controller coordinates the read and write positions and slot availability.

At RX side there is an RXGET register, which tells if a filled slot is available, when yes, then at which address the packet data starts and how many bytes were actually filled. Writing zero into the RXGET register releases the filled slot and makes it available for another packet receival, and the RXGET register advances to the next filled slot.

At TX side TXPUT register tells if an empty slot is available and its TXMEM word address. Writing the FILLED flag and the FBYTES field into the TXPUT register will schedule the packet for sending and the TXPUT register advances to the next empty slot.

The NV APB ETH also provides an MDIO module to configure the Ethernet phy and to poll its status.

# APB Registers

APB Address	Reg. Name	Description
0000	VERSION (RO)	bit 15-0: VER_INC (BCD): incremented at every change / bit 23-16: VERSION (BCD), 0x10 = 1.0 / bit 31-24: MODID = 0xE0
0004	INFO (RO)	bit 3-0: TXMEM_ABITS, 10 = 4kByte, 12 = 16 kByte / bit 7-4: RXMEM_ABITS, 10 = 4kByte, 12 = 16 kByte / bit 31-24: reserved
0008	TXCTRL	bit 11-0: TX_SLOT_SIZE: in 32-bit units / bit 29-12: reserved / bit 30: MANUAL_CRC: 1 = CRC included in the TX slot / bit 31: TXEN: enable TX
000C	RXCTRL	bits 11-0: RX_SLOT_SIZE: in 32-bit units / bit 28-12: reserved / bit 29: IGNORE_ERR: 1 = accept packages with CRC errors / bit 30: PROMISC: 1 = ignore target MAC address / bit 31: RXEN: enable RX / The RX_SLOT_SIZE can not be changed after RXEN=1.
0010	PHYCTRL	bit 1-0: SPEED: PHY speed 0 = 10 MBit/s, 1 = 100 MBit/s, 2 = 1000 MBit/s / bit 17-16: DET_SPEED: detected PHY speed (RO) (for gigabit phy-s)
0014	(reserved)
0018	MACADDR1	bits31-0: MAC Address bits 31-0
001C	MACADDR2	bits15-0: MAC Address bits 47-32 / bits 31-16: reserved

0020	MDIO_CMD	bit 15-0: WR_DATA / bit 20-16: REG_ADDR / bit 25-21: PHY_ADDR / bit 26: PHY_RESET (positive logic, manual clear) / bit 30: WRITE_NREAD: 1 = write, 0 = read / bit 31: START
0024	MDIO_STATUS	bit 15-0: RD DATA / bit 20-16: REGADDR / bit 25-21: PHY_ADDR / bit 30: WRITE_NREAD / bit 31: BUSY
0028	MDIO_SPEED	Bit7-0: half MDIO bit APB clocks / Default: 20 = 0x14
002C	(reserved)
0030	TXPUT	bit 11-0: SLOT_ADDR (RO) (in 32-bit units) / bit 23-12: FILLED_BYTES (RW) / bit 30-24: reserved / bit 31: FILLED (RW) / When writing the FILLED with 1, the TX unit advances to the next slot, if the FILLED was previously 0.
0040	RXGET	bit 11-0: SLOT_ADDR (RO) (in 32-bit units) / bit 23-12: FILLED_BYTES (RO) / bit 30-24: reserved / bit 31: FILLED / RELEASE (RW) / When writing the FILLED with 0, the RX unit advances to the next slot, if the FILLED was previously 1.
4000	TXRAM	Write only memory for the TX Packets. Only 32-bit write acces is allowed. The next packet data must be filled at TXPUT.SLOT_ADDR * 4. / Size can be determined by TXMEM_ABITS (reg 0x0004): / TXMEM Bytes = 2 ^ (TXMEM_ABITS + 2)
8000	RXRAM	Read only memory for the RX packets. The actual packet data can be read at TXGET.SLOT_ADDR * 4. / Size can be determined by RXMEM_ABITS (reg 0x0004): / RXMEM Bytes = 2 ^ (RXMEM_ABITS + 2)